## Slide 1: Guide to Network Defense and Countermeasures Third Edition
Chapter 6
Wireless Network Fundamentals

## Slide 2: Objectives
Explain wireless communication concepts
Describe radio frequency characteristics relevant to wireless networking

## Slide 3: Wireless Communications Primer
Wireless networking: any exchange of data between computers and other devices that does not use cables
Different from cabled networks:
  Use certain types of electromagnetic radiation
    Radio frequency (RF) waves is most commonly used
    Infrared (IR) radiation used mainly for communication with peripheral devices

## Slide 4: Electromagnetic Radiation
Electromagnetic (EM) radiation: electromagnetic energy traveling as a self-propagating wave and spreading out at the same time
Wave: means of transporting energy from one place to another
  Energy is transported by a disturbance that occurs in a distinct repeating pattern
Amplitude: maximum departure of a wave from the undisturbed state
Frequency: number of times an event occurs in a specified period (measured in hertz)

## Slide 5: Electromagnetic Radiation
Wavelength: distance between repeating units of the wave (usually the midpoint or crest)
Frequency has an inverse relationship with wavelength
  Frequency is number of waves per second
  Wavelength is the distance between waves
Figure 6-1 Wave properties

## Slide 6: Infrared Transmissions
Infrared transmissions use infrared light pulses
  Require an emitter (laser diode or LED) and a detector (sometimes combined with an emitter)
  Intensity of the light pulse indicates the on or off status of each bit of data
Directed IR transmission: requires emitter and detector to be pointed directly at one another
Diffused IR transmission: relies on reflected light that can bounce off walls or other objects

## Slide 7: Infrared Transmissions
Advantages of IR wireless:
  Does not interfere with other signals and is not susceptible to interference from them
  IR signals cannot pass through walls
Disadvantages of IR wireless:
  Limited range
  Low speeds of up to 4 Mbps
  Requires direct line of sight or in-the-room conditions

## Slide 8: Radio Frequency Transmissions
RF is the most commonly used transmission medium for WLANs
RF can travel through walls and travel great distances
RF involves transmission ranges, signal modulation, and interference
  More complex than IR

## Slide 9
Table 6-1 Common RF bands

## Slide 10: Transmission Ranges
Transmission ranges vary depending on the standard in use and environment
Generally, lowering bandwidth increases coverage area
  The rate at which a wireless client receives data decreases as client moves away from transmitter
Access point: an electronic device that connects to a wired network and can transmit and receive wireless signals
  Enforcing security for wireless signals requires careful placement of APs

## Slide 11: Interference
Co-channel interference occurs when signals from APs interfere with each other
  Must arrange APs so that overlapping signals do not share the same channel (frequency)
Interference
  RF can be highly susceptible to interference from electrical storms, solar activity, laser printers, and other forms of EM radiation (microwave ovens)
  Multipath: a signal has more than one path from transmitter to receiver
    If signal is reflected, the reflected path can interfere with direct path (this problem is called fading)

## Slide 12: Radio Frequency Signal Behavior
RF signal behavior is characterized by whether a factor contributes to an increase (gain) or decrease (loss) in power
  Gain: positive difference in amplitude between two signals
    Achieved by magnifying the signal
  Loss: negative difference in amplitude of signals (sometimes called attenuation)
Common factors that result in loss:
  Absorption – when certain types of material absorb RF signals, such as wood, concrete, and asphalt
  Reflection – when RF signals bounce off some materials

## Slide 13: Radio Frequency Signal Behavior
Common factors that result in loss (cont’d):
  Scattering – when small objects and rough textures disperse signals
  Refraction – when differences in density between air masses over distances cause problems (signals may bend instead of traveling in a straight line)
  Diffraction – similar to refraction, except signal bends around an object in its path
  Voltage standing wave ratio (VSWR) – caused by differences in equipment rather than external influences

## Slide 14: Measuring RF Signals
RF power is measured on a linear scale using milliwatts (mW)
  Watt: measure of power or the rate at which work is done
  One mW is equal to one-thousandth of one watt
Decibel-milliwatts (dBm) is the reference point that relates the decibel scale to the linear milliwatt scale
  Specifies that 1 mW = 0 dBm
  RF power gains and losses on a relative scale are measured in decibels (dB) instead of mW

## Slide 15
Table 6-3 The 10s and 3s rules of RF math

## Slide 16: Measuring RF Signals
Equivalent Isotropically Radiated Power (EIRP): power radiated by a wireless system’s antenna
  Uses a measurement known as isotropic decibels (dBi) that applies only to an antenna’s gain
Transmitter Power Output (TPO) measures the power being delivered to the transmitting antenna

## Slide 17: RF Signaling
RF transmits a carrier signal
  Changes based on the signal’s voltage and direction
RF data is transmitted as analog or digital signals
  Analog RF signal: continuous wave that oscillates between positive and negative voltage
    Must be converted into digital format
  Digital RF signal: divided into discrete segments or defined states within the carrier’s range
Modulation: changing characteristics of the signal
Three characteristics of a carrier signal can be modified to enable it to carry data: height, frequency, and relative starting point of the signal

## Slide 18: Analog Modulation
Analog modulation methods:
  Amplitude modulation (AM) – the height of the carrier wave is changed so a higher wave represents a 1 bit and a lower wave represents a 0 bit
  Frequency modulation (FM) – number of waves representing one cycle is changed so that the number representing a 1 bit is greater
  Phase modulation (PM) – cycle’s starting point is changed when the bit being transmitted changes from 1 to 0

## Slide 19
Figure 6-3 Analog modulation techniques

## Slide 20: Digital Modulation
Digital modulation techniques are superior to analog methods for four reasons:
  More efficient use of bandwidth
  Fewer interference problems
  Error correction that is more compatible with other digital systems
  Less power required to transmit

## Slide 21: Digital Modulation
Three binary signaling techniques:
  Return-to-zero (RTZ) – Voltage increases to represent a 1 bit, no voltage represents a 0 bit
    Voltage for a 1 bit drops back to zero before the end of the bit period
  Non-return-to-zero (NRZ) - Voltage increases to represent a 1 bit, no voltage represents a 0 bit
    Voltage for a 1 bit does not drop back to zero before the end of the bit period
  Polar non-return-to-zero (polar NRZ) – Voltage increases to represent a 1 and drops to negative voltage to represent a 0 bit

## Slide 22: Digital Modulation
RF signals are narrowband transmissions
  Transmit on one frequency or small frequency range
Common digital modulation methods:
  Amplitude shift keying (ASK) – height of the carrier can be changed to represent a 1 or 0 bit
  Frequency shift keying (FSK) – carrier signal’s frequency is changed to represent a 1 or 0 bit
  Phase shift keying (PSK) – similar to phase modulation
  Frequency division multiplexing (FDM) – multiple base signals are modulated on different carrier waves and combined to form a composite signal

## Slide 23
Figure 6-4 Narrowband transmission

## Slide 24: Spread Spectrum
Spread spectrum spreads a signal over a broader portion of the radio band
Advantages of spread spectrum over narrowband:
  Bandwidth of signal is higher than original message
  Bandwidth is determined by the spreading function
    Known only to the transmitter and receiver
In spread spectrum:
  The spreading function attaches a key (called a spreading code or sequence) to the communication channel

## Slide 25
Figure 6-5 Spread-spectrum transmission

## Slide 26: Spread Spectrum
Major methods of spread spectrum:
  Direct sequence spread spectrum (DSSS) – key is applied at the data level
  Frequency hopping spread spectrum (FHSS) – key is applied at the carrier frequency level
  Orthogonal frequency division multiplexing (OFDM) – high-speed signal is divided into smaller pieces and sent simultaneously across lower-speed channels

## Slide 27
Figure 6-6 DSSS transmission

## Slide 28
Figure 6-7 FHSS transmission

## Slide 29: Spread Spectrum
In DSSS, an expanded redundant chipping code is used to transmit each bit
  Chipping code: term for bit pattern
  DSSS is less vulnerable to data loss from interference but requires high bandwidth
In FHSS, carrier hops frequencies over a wide band according to a sequence defined by the key
  Key is called the hopping code and it determines the sequence and speed of frequency hops
  Advantages of FHSS are immunity to jamming and interference and it is secure

## Slide 30: Wireless LANs and Their Components
To secure a WLAN, you need to be familiar with:
  Wireless components
  Topologies
  Transmission and frequency ranges
  Methods of identifying and eliminating interference sources

## Slide 31: Wireless NICs
When a wireless NIC (WNIC) prepares to transmit, it does the following:
  Changes the computer’s internal data from parallel to serial transmission
  Divides data into packets and attaches address information
  Determines where to send the packet
  Transmits the packet

## Slide 32
Figure 6-8 Desktop computer WNICs

## Slide 33: Access Points
Access point (AP) - an antenna and radio transceiver used to transmit and receive signals and to perform the following functions:
  Acts as a base station for the wireless network segment
  Serves as the bridge between wired and wireless segments
Preferred placement of APs is on the ceiling or high on a wall
  Solution to getting power to APs placed in ceilings or up high: Power over Ethernet (PoE)
    PoE: power for AP unit is supplied through unused wires in Ethernet cabling

## Slide 34
Figure 6-9 Wireless Access Point

## Slide 35: Antennas
RF waves are transmitted and received by an antenna
EIRP is the measurement of total power radiated by a wireless system’s antenna
  FCC uses the term intentional radiator to describe a device designed to generate radio signals
Fundamental characteristics of antennas:
  As frequency gets higher, wavelength gets smaller (requiring a smaller antenna)
    Antenna length should be ¼ of the wavelength
  As antenna gain increases, coverage area narrows

## Slide 36
Figure 6-10 Antenna sending and receiving radio signals

## Slide 37: Antennas
Other characteristics of RF antenna transmissions:
  Polarization – plane in which radio waves propagate or the orientation of radio waves as they leave the antenna
  Wave propagation – dispersal pattern of waves as they travel from sending to receiving antennas
  Fresnel zone – series of ellipsoidal shapes in the wave calculated to determine the signal strength
    Also identifies potential obstacles and multipath distortion between antennas
  Free space path loss – phenomenon of signals dispersing as they travel from the sending antenna
    Signal becomes weaker

## Slide 38
Figure 6-11 The Fresnel zone

## Slide 39: Antennas
There are three basic types of antennas: omnidirectional (also known as dipole), semidirectional, and highly directional
Table 6-4 Basic antenna types

## Slide 40: Remote Wireless Bridges
Remote wireless bridges connect wired and wireless segments like APs, with two exceptions:
  Transmits at higher power than an AP
  Uses a directional antenna to focus transmission in one direction
    APs use omnidirectional transmission
Operates in four modes:
  Access point mode
  Root mode
  Nonroot mode
  Repeater mode

## Slide 41
Figure 6-12 Point-to-point wireless bridging

## Slide 42
Figure 6-13 Point-to-multipoint wireless bridging

## Slide 43: Wireless Gateways
Wireless gateway combines management and security into a single appliance
Can perform the following functions:
  Authentication
  Encryption
  Intrusion detection
  Malicious program protection
  Bandwidth management
  Centralized network management

## Slide 44: WLAN Configurations
Three basic WLAN configurations:
  Basic Service Set (BSS) – group of wireless devices are served by a single AP
    Must be assigned a unique identifier known as the service set identifier (SSID)
    Geographical coverage is called the Basic Service Area (BSA)
  Extended Service Set (ESS) – APs are set up to provide overlap
    Coverage areas are called cells and movement between cells is called roaming
  Independent Basic Service Set (IBSS) – wireless network that does not use an AP

## Slide 45
Figure 6-14 BSS configuration

## Slide 46
Figure 6-15 ESS configuration

## Slide 47: Wireless Networking Standards
Wireless networking technology was developed in a haphazard way
  Different companies worked on similar problems and came up with different solutions
Wireless standards process has become more efficient
  Still overlaps and uncertainty as wireless networking expands

## Slide 48: IEEE 802.11
IEEE 802.11 – first released in 1997
  Most recent iteration is IEEE Std. 802.11-2007
    Includes all ongoing amendments up to that time
    Since 2007, 802.11n (2009) have been added
IEEE 802.11b (1999) – ratified before 802.11a
  Operates in the 2.4 GHz band and maximum bandwidth supported is 11 Mbps
  No longer used in contemporary WLANs
IEEE 802.11a (1999) – ratified after 802.11b
  Operates in the 5 GHz band
    Not subject to interference by microwave ovens and cordless phones that operate in 2.4 GHz range
    Maximum bandwidth is 54 Mbps

## Slide 49: IEEE 802.11
802.11g (2003) – operates in the 2.4 GHz band
  Interoperable with 802.11a devices
  Maximum bandwidth is 54 Mbps
802.11i (2004) – wireless security standard
  WPA 2 was released to map exactly to the 802.11 standard
802.11r (2008) – designed to provide fast basic service set transition (FT)
  Involves having a client perform a security association with the next AP before the client leaves the range of the current AP

## Slide 50: IEEE 802.11
802.11n (2009) – defines a standard that supports multiple-input multiple-output (MIMO)
  Uses both 2.4 GHz and 5 GHz radio frequencies to simultaneously send or receive data
  Maximum bandwidth can reach 450 Mbps
802.11v (2011) – defines standards that allow wireless stations to exchange operational information to improve wireless network performance
802.11ac (Draft) – will use the 5 GHz band
  Expected to provide multistation WLANs with a bandwidth of 1 Gbps

## Slide 51: Radio Frequency and the FCC
Wireless primarily uses RF
  Can interfere with critical applications
Regulated strictly by the Federal Communications Commission (FCC)
  Regulates what frequencies wireless communications can use, how much power antennas can emit, and other matters concerning the use of radio waves, infrared, and microwaves for communication
When planning deployment, check with your local FCC office to learn about regulations or requirements you must meet

## Slide 52: Summary
Wireless transmissions use electromagnetic (EM) radiation, specifically radio frequency (RF) waves or infrared (IR) radiation, to communicate
EM radiation travels in waves
The RF spectrum is divided into bands based on frequency
The speed and transmission range of a wireless network vary depending on the standard, equipment, environmental factors, number of users, location of clients, and purpose

## Slide 53: Summary
RF transmits a carrier signal
RF data can be analog or digital
Spread spectrum spreads a narrowband signal over a broader portion of the RF band
Wireless network components include wireless NICs, access points, antennas, remote wireless bridges, and wireless gateways
Antennas transmit and receive radio waves and can be omnidirectional, semidirectional, or highly directional

## Slide 54: Summary
A remote wireless bridge operates in four modes: access point, root, nonroot, and repeater
IEEE 802.11 standards define three WLAN configurations: BSS, ESS, and IBSS
IEEE 802.11 standards include: 802.11a, 802.11g, and 802.11n
RF is subject to strict regulations by the FCC because of the potential for interference with critical communications, including radio, TV, military, and emergency services