## Slide 1: Guide to Network Defense and Countermeasures Third Edition
Chapter 2
TCP/IP

## Slide 2: Objectives
Explain the fundamentals of TCP/IP networking
Describe IPv4 packet structure and explain packet fragmentation
Describe Internet Protocol version 6 (IPv6)

## Slide 3: The OSI Model and TCP/IP Protocols
Transmission Control Protocol/Internet Protocol (TCP/IP) is a suite of many protocols for transmitting information from point to point on a network
  Often referred to as a “stack”
This section covers:
  Open System Interconnection (OSI) model
  IP addressing
  subnetting

## Slide 4: The OSI Model
OSI reference model: divides the communication functions used by two hosts into seven separate layers
TCP/IP has its own stack of protocols that correspond to these layers
Table 2-1 The OSI model and the subprotocols of the TCP/IP stack

## Slide 5: The OSI Model
TCP/IP subprotocols are services that support a number of network functions:
  HTTP (Hypertext Transfer Protocol)
  DNS (Domain Name System)
  DHCP (Dynamic Host Configuration Protocol)
  FTP (File Transport Protocol)
  SNMP (Simple Network Management Protocol)
  Telnet
  IMAP, SMTP, POP

## Slide 6: TCP/IP Addressing
IP addresses are a method used to identify computers
  Processed at the Network layer of the OSI model
  Most common in use conform to Internet Protocol version 4 (IPv4)
    32-bit address divided into four groups called octets
    Each octet contains 8 bits of data
  In binary, an IP address looks like:
    10000000.00100110.00101100.11100010
  Binary is converted to dotted decimal notation
    192.168.10.1

## Slide 7: TCP/IP Addressing
IP address components
  Network identifier – shared among computers in a network segment
  Host address – unique to each computer on the network segment
Subnet mask – used to identify which part of the IP address is the network identifier and which is the host identifier
Attackers can gain access to a network by determining IP addresses of computers
IP addresses need to be concealed to prevent certain attacks

## Slide 8: TCP/IP Addressing
If an attacker can find a PC’s IP address, they can run a port scan to look for open ports to exploit
To hide addresses, use Network Address Translation (NAT)
  Translates private network’s internal addresses into external addresses that can be used on the public Internet
    Private network’s internal addresses are not routable on the Internet
Today IP addresses are in short supply, so Internet Protocol version 6 (IPv6) is being implemented

## Slide 9: Address Classes
IPv4 addresses are separated by classes
  Class is determined by the number of its networks compared to number of hosts
  Example: a Class A address uses 8 bits for the network portion and 24 bits for the host portion

## Slide 10
Table 2-2 IP address classes

## Slide 11: Private IP Address Ranges
Private addresses are needed so that organizations can build internal infrastructures
  Public IP addresses require registration and a fee for each address
  Private addressing scheme eliminates the need to purchase addresses for every group of machines
Table 2-3 Private IP address ranges

## Slide 12: Subnetting
Address classes already have network id octets by default
  Class A uses first octet
  Class B uses first two octets
  Class C uses first three octets
Default Class B has 16 bits available for hosts
  This means a Class B network can have more than 65,000 host addresses
  Some of host bits can be used to identify the network
  Creates smaller subnetworks with fewer hosts

## Slide 13: Subnetting
Subnetting can be used for:
  Mirroring the organization’s physical layout
  Mirroring the organization’s administrative structure
  Planning for future growth
  Reducing and controlling network traffic
  Increasing network security
If all users with similar security and access needs are grouped into a single subnet, the entire group can be managed instead of managing each user separately

## Slide 14: Subnetting
Subnetting
  Borrow bits from host portion of IP address
  Number of borrowed bits determines how many subnets and hosts are available
  At least two bits must be available for hosts
    Up to 14 bits can be borrowed for a Class B network

## Slide 15
Table 2-4 Class B subnetting

## Slide 16
Table 2-5 Binary-to-decimal values

## Slide 17: Subnetting
Subnetting a Class C address example:
  Network address: 199.1.10.0
  Default subnet mask: 255.255.255.0
  Selected mask: 255.255.255.224
  Mask in binary: 11111111.11111111.11111111.11100000
    Last masked digit occupies the binary value of 32
    Starting with network address, increment by 32 until you reach the mask’s number (224)

## Slide 18
Table 2-6 Subnetting example

## Slide 19: Variable Length Subnet Masking
Networks that do not have a large number of available IP addresses use variable length subnet masking (VLSM)
  Involves applying masks of varying sizes to the same network
  Creates subnets within subnets
  Often used to secure stub networks (only have one connection to any other network

## Slide 20: Classless Interdomain Routing
Classless Interdomain Routing (CIDR) – specifies the number of masked bits in an IP address/subnet mask combination
Example:
  A network address of 192.168.6.0 with a subnet mask of 255.255.255.224 would have a CIDR notation of 192.168.6.0/27
CIDR overcomes limitations of default subnet masks so that unused addresses do not go to waste

## Slide 21: Unicasting, Multicasting, and Broadcasting
Unicast transmission: one packet is sent from one server to each client computer individually
Multicast transmission: server can treat several computers as a group and send one transmission that reaches all of them
  Example: streaming video presentation
Broadcast transmission: sent to all nodes on a specific network
  Flooded broadcasts: sent to any subnet
  Directed broadcasts: sent to a specific subnet

## Slide 22: Examining Internet Protocol Version 4 (IPv4)
IP datagrams
  Portion of the packet that is responsible for routing through networks
  Processed at the Network layer of the OSI model
  Complete message is transmitted using multiple datagrams
  Contain information about source and destination IP addresses, control settings, and data
  Divided into different sections
    Primary subdivisions are header and data
    Some packets have a footer (or trailer) that indicates the end of a packet or error checking (CRC)

## Slide 23: IP Header Structure
Part of an IP packet that computers use to communicate
IP header plays an important role in terms of network security and intrusion detection
Contains a number of fields and is similar to a TCP header

## Slide 24
Figure 2-1 IP header structure

## Slide 25: IP Header Structure
Most network operating systems (NOSs) have a type of built-in or add-on program to monitor network activity
Most administrators prefer third-party applications for their versatility and extra features
  Wireshark (formerly Ethereal) is an example

## Slide 26
Figure 2-2 IP header structure as seen in a Wireshark packet capture

## Slide 27: ICMP Messages
Internet Control Message Protocol (ICMP) used to assist with troubleshooting communication problems
  Ping command uses ICMP to check whether a remote host has connectivity
Processed at the network layer of the OSI model
Firewalls or packet filters can be configured to accept or deny certain ICMP packets through the network
  Some ICMP packets could be used as part of an attack

## Slide 28
Table 2-7 ICMP types

## Slide 29: TCP Headers
TCP/IP packets may also contain TCP headers
  TCP headers are processed at the Transport layer of OSI model
  TCP portion of a packet is called TCP segment
  Flags section of a TCP header are important:
    You can specify them when you create packet-filtering rules

## Slide 30
Figure 2-3 TCP header structure

## Slide 31: UDP Headers
User Datagram Protocol (UDP): provides a transport service for IP
  Processed at Transport layer of OSI model
  Considered unreliable because it is connectionless
    UDP packet does not contain sequence or acknowledgement numbers that enable TCP to guarantee delivery
  Much faster than TCP
  Used for broadcasting messages or for protocols that do not require the same level of service as TCP
  Attackers can scan for open UDP services

## Slide 32
Figure 2-5 UDP header structure

## Slide 33: Packet Fragmentation
Originally developed to allow large packets to pass through routers with frame size limitations
  Routers divide packets into multiple fragments and send them along the network
Fragmentation creates security problems
  Port numbers appear only in fragment 0
  Fragments 1 and higher pass through filters without being scrutinized
    Attacker can modify the IP header to make all fragment numbers start at 1 or higher
  Configure firewall to drop all fragmented packets

## Slide 34: The TCP Life Cycle and the TCP Three-Way Handshake
Establishing connection-oriented communication using a three-way handshake:
  Host A sends an initial sequence number in its first packet to Host B
    Called a SYN packet
  Host B receives SYN packet - responds with SYN ACK with an initial sequence number for Host B
    Includes an acknowledgement number that is one more than the initial sequence number
  Host A sends an ACK packet to Host B
    Increases Host B’s sequence number by one

## Slide 35
Table 2-8 TCP three-way handshake: SYN
Table 2-9 TCP three-way handshake: SYN ACK

## Slide 36
Table 2-10 TCP three-way handshake: ACK

## Slide 37: The TCP Life Cycle and the TCP Three-Way Handshake
Sliding window size: determines the number of packets that can be sent before ACKs must be received
  Controls the flow and efficiency of communications
  Sender controls size of sliding window
FIN flag is set when either side is ready to end the session
  Station that receives the initial flag sends a response packet with the ACK flag and its own FIN flag set to acknowledge receipt and to show it is ready to end the session

## Slide 38
Figure 2-7 Summary of the TCP three-way handshake

## Slide 39: Domain Name Service
DNS servers translate fully qualified domain names (FQDNs) to IP addresses
DNS can be used to block unwanted communications
  Administrators can block Web sites containing offensive content
DNS attacks
  Buffer overflow
  Zone transfer
  Cache poisoning

## Slide 40: Internet Protocol Version 6 (IPv6)
IPv6 addresses the many limitations of IPv4
  IPv6 has a larger address space of 128 bits
  Routing tables need only the entries of other routers that are directly connected to them
  IPv6 has integrated support for security called IPsec
  Network Address Translation (NAT) is not needed
    NAT has security problems
  IPv6 can determine its own settings based on two different models:
    Stateful autoconfiguration
    Stateless autoconfiguration

## Slide 41: IPv6 Core Protocols
IPv6 has major differences to IPv4 in its core architecture and functions
  It is a connectionless, unreliable datagram protocol used mainly for addressing and routing packets
IPv6 datagram consists of the IPv6 header and IPv6 payload
  Header is made up of IPv6 base header and optional extension headers

## Slide 42
Figure 2-8 IPv6 header structure

## Slide 43: IPv6 Core Protocols
Extension headers are not normally found in a typical IPv6 packet
  If needed, the sending host adds appropriate header
  IPv6 extension headers:
    Hop-by-Hop Options
    Destination Options
    Routing
    Fragment
    Authentication
    Encapsulating Security Payload (ESP)

## Slide 44: Internet Control Message Protocol for IPv6
ICMPv6 messages are grouped into two classes:
  Error messages: 0-127
  Informational messages: 128-255
ICMPv6 messages is preceded by an IPv6 header
  Sometimes by extension headers
Type field contains the value for a type of message
Table 2-11 Common ICMPv6
message type codes

## Slide 45
Table 2-12 ICMPv6 features

## Slide 46: Multicast Listener Discovery
Multicasts: connectionless delivery of information to multiple subscribers at the same time
  Has a single stream on any link instead of one stream per recipient
IP multicast traffic is sent to a single address but is processed by all members of a multicast group
  Hosts listening on a specific multicast address are part of the multicast group
  Group membership is dynamic
  Members can be on different subnets

## Slide 47: Multicast Listener Discovery
Multicast Listener Discovery (MLD) enables IPv6 routers to discover multicast listeners and decide which multicast addresses are of interest to nodes
Table 2-13 Multicast Listener Discovery message types

## Slide 48: Neighbor Discovery
Neighbor Discovery (ND): new IPv6 protocol that replaces ARP, ICMP Router Discovery and ICMP Redirect in IPv4
  Uses ICMPv6 messages to manage node-to-node communications
Five different types of ICMP messages:
  Router Solicitation
  Router Advertisement
  Neighbor Solicitation
  Neighbor Advertisements
  Redirect

## Slide 49
Table 2-14 IPv6 Neighbor Discovery functions

## Slide 50: IPv6 Addressing
IPv6 addresses:
  128 bits long and use the hexadecimal numbering format
  Consist of eight hex groups separated by colons
    Each hex group contains a 16-bit value
Examples:
  4EDC:0000:7654:3210:F3DC:BA98:7654:AB1F
  Including leading zeros is not necessary
    1080:0:0:0:8:800:200C:417A
  Can replace consecutive zeros with a double colon
    1080::8:800:200C:417A

## Slide 51: IPv6 Addressing
Unicast addressing: used for one-to-one communication (between two host or two routers)
Scopes of unicast addresses:
  Global unicast address: public addresses routable on the Internet
  Site-local unicast address: similar to private IPv4 addresses
  Unique local IPv6 unicast address: replacing site-local unicast address
  Link-local unicast address: used by hosts to communicate with other hosts on same network

## Slide 52: IPv6 Addressing
Multicast addresses: used for one-to-many communications
  Always begin with FF in the first byte
Anycast addresses: used for one-to-one or one-to-many communications
  Created automatically when a unicast address is assigned to more than one interface
  Offers flexibility in providing services
  Currently only used by routers but will expand as technology becomes widespread

## Slide 53: IPv6 Configuration
Microsoft OSs since Windows XP SP1 have built-in support for IPv6 support
  Support stateless autoconfiguration
A link-local address is assigned to every Ethernet interface during startup
  Assigned automatically based on receipt of IPv6 Router Advertisement messages
  Must have a correctly configured IPv6 capable router on network segment

## Slide 54: IPv6 Utilities
Ipconfig: shows IPv6 configuration details
  Can also use the command with IPv4
Figure 2-10 Using the ipconfig command

## Slide 55: IPv6 Utilities
Netstat: display system’s routing tables by using netstat –r command
  Netstat -n option shows current sessions with the associated port numbers
  Netstat –ps IPv6 option displays detailed statistics on IPv6 activity since the last boot
Netsh: command-line scripting tool on Windows systems that allows troubleshooting and configuration of network interfaces

## Slide 56: Summary
TCP/IP is a suite of protocols for transmitting information from point to point on a network
TCP and UDP map to the Transport layer and IPv4, IPv6, ICMP, and ICMPv6 map to the Network layer of the OSI model
IP addresses most commonly used on the Internet conform to IPv4
You must understand the normal configuration of fields in IP, TCP, and UDP headers to recognize and filter unwanted or malicious traffic

## Slide 57: Summary
Fragmentation of IP packets allows large packets to pass through routers with frame size limits
DNS translates fully qualified domain names into IP addresses
TCP three-way handshake establishes a reliable connection between two points
IPv6 was designed to address problems with IPv4
IPv6 is a connectionless, unreliable protocol used mainly for addressing and routing packets
ICMP is used for reporting errors and diagnostics

## Slide 58: Summary
MLD enables IPv6 routers to discover multicasts
IPv6 uses ND to perform tasks that ARP, ICMP Router Discovery and ICMP Redirect handled
Hexadecimal numbering format makes IPv6 addresses manageable
IPv6 uses three types of addresses: unicast, multicast, and anycast
You can monitor and configure IPv6 using tools such as Ipconfig, Netstat, and Netsh